Annex XV dossier

HANDOVER FILE

This Annex XV template has been completed and submitted by the Lead Development Association International (co-ordinators of the VRAL) in order to formally hand over to the European Chemicals Agency the VRAL risk assessment reports.  The risk assessment reports themselves are being submitted as appendices to this Annex XV handover file (see “Other information” section at end of this Handover file).

Substance Name, EC Number, CAS Number:

| Substance | CAS Number | EINECS Number |
| --- | --- | --- |
| Lead | 7439-92-1 | 231-100-4 |
| Lead oxide | 1317-36-8 | 215-267-0 |
| Lead tetroxide | 1314-41-6 | 215-235-6 |
| Dibasic lead phthalate | 69011-06-9 | 273-688-5 |
| Basic lead sulphate | 12036-76-9 | 234-853-7 |
| Tribasic lead sulphate | 12202-17-4 | 235-380-9 |
| Tetrabasic lead sulphate | 12065-90-6 | 235-067-7 |
| Neutral lead stearate | 1072-35-1 | 214-005-2 |
| Dibasic lead stearate | 12578-12-0 | 235-702-8 |
| Dibasic lead phosphite | 12141-20-7 | 235-252-2 |
| Polybasic lead fumarate | 90268-59-0 | 290-862-6 |
| Basic lead carbonate | 1319-46-6 | 215-290-6 |
| Basic lead sulphite | 62229-08-7 | 263-467-1 |

CONTENTS

Restriction proposal	7

Information on hazard and risks	8

1	identity of the substance and physical and chemical properties	8

1.1	Name and other identifiers of the substance	8

1.2	Composition of the substance	8

1.3	Physico-chemical properties	9

2	maNufacture and uses	10

2.1	Manufacture	10

2.2	Identified uses	10

2.3	Uses advised against	10

3	classification and labelling	11

3.1	Classification in Annex I of Directive 67/548/EEC	11

3.2	Self classification(s)	11

4	environmental fate properties	12

4.1	Degradation	12

4.1.1	Stability	12

4.1.2	Biodegradation	12

4.1.2.1	Biodegradation estimation	12

4.1.2.2	Screening tests	12

4.1.2.3	Simulation tests	12

4.1.3	Summary and discussion of persistence	12

4.2	Environmental distribution	12

4.2.1	Adsorption/desorption	12

4.2.2	Volatilisation	12

4.2.3	Distribution modelling	12

4.3	Bioaccumulation	12

4.3.1	Aquatic bioaccumulation	12

4.3.1.1	Bioaccumulation estimation	12

4.3.1.2	Measured bioaccumulation data	12

4.3.2	Terrestrial bioaccumulation	12

4.3.3	Summary and discussion of bioaccumulation	12

4.4	Secondary poisoning	12

5	Human health hazard assessment	13

5.1	Toxicokinetics (absorption, metabolism, distribution and elimination)	13

5.2	Acute toxicity	13

5.2.1	Acute toxicity: oral	13

5.2.2	Acute toxicity: inhalation	13

5.2.3	Acute toxicity: dermal	13

5.2.4	Acute toxicity: other routes	13

5.2.5	Summary and discussion of acute toxicity	13

5.3	Irritation	13

5.3.1	Skin	13

5.3.2	Eye	13

5.3.3	Respiratory tract	13

5.3.4	Summary and discussion of irritation	13

5.4	Corrosivity	13

5.5	Sensitisation	13

5.5.1	Skin	13

5.5.2	Respiratory system	13

5.5.3	Summary and discussion of sensitisation	13

5.6	Repeated dose toxicity	14

5.6.1	Repeated dose toxicity: oral	14

5.6.2	Repeated dose toxicity: inhalation	14

5.6.3	Repeated dose toxicity: dermal	14

5.6.4	Other relevant information	14

5.6.5	Summary and discussion of repeated dose toxicity:	14

5.7	Mutagenicity	14

5.7.1	In vitro data	14

5.7.2	In vivo data	14

5.7.3	Human data	14

5.7.4	Other relevant information	14

5.7.5	Summary and discussion of mutagenicity	14

5.8	Carcinogenicity	14

5.8.1	Carcinogenicity: oral	14

5.8.2	Carcinogenicity: inhalation	14

5.8.3	Carcinogenicity: dermal	14

5.8.4	Carcinogenicity: human data	14

5.8.5	Other relevant information	14

5.8.6	Summary and discussion of carcinogenicity	14

5.9	Toxicity for reproduction	15

5.9.1	Effects on fertility	15

5.9.2	Developmental toxicity	15

5.9.3	Human data	15

5.9.4	Other relevant information	15

5.9.5	Summary and discussion of reproductive toxicity	15

5.10	Other effects	15

5.11	Derivation of DNEL(s) or other quantitative or qualitative measure for dose response	15

5.11.1	Overview of typical dose descriptors for all endpoints	15

5.11.2	Correction of dose descriptors if needed (for example route-to-route extrapolation)	15

5.11.3	Application of assessment factors	15

5.11.4	Selection/ identification of the critical DNEL(s)/ the leading health effect	15

6	Human health hazard assessment of physico-chemical properties	16

6.1	Explosivity	16

6.2	Flammability	16

6.3	Oxidising potential	16

7	Environmental hazard assessment	17

7.1	Aquatic compartment (including sediment)	17

7.1.1	Toxicity test results	17

7.1.1.1	Fish	17

Short-term toxicity to fish	17

Long-term toxicity to fish	17

7.1.1.2	Aquatic invertebrates	17

Short-term toxicity to aquatic invertebrates	17

Long-term toxicity to aquatic invertebrates	17

7.1.1.3	Algae and aquatic plants	17

7.1.1.4	Sediment organisms	17

7.1.1.5	Other aquatic organisms	17

7.1.2	Calculation of Predicted No Effect Concentration (PNEC)	17

7.1.2.1	PNEC water	17

7.1.2.2	PNEC sediment	17

7.2	Terrestrial compartment	17

7.2.1	Toxicity test results	17

7.2.1.1	Toxicity to soil macro organisms	17

7.2.1.2	Toxicity to terrestrial plants	17

7.2.1.3	Toxicity to soil micro-organisms	17

7.2.1.4	Toxicity to other terrestrial organisms	17

Toxicity to birds	17

Toxicity to other above ground organisms	17

7.2.2	Calculation of Predicted No Effect Concentration (PNEC_soil)	18

7.3	Atmospheric compartment	18

7.4	Microbiological activity in sewage treatment systems	18

7.4.1	Toxicity to aquatic micro-organisms	18

7.4.2	PNEC for sewage treatment plant	18

7.5	Calculation of Predicted No Effect Concentration for secondary poisoning (PNEC_oral)	18

7.6	Conclusion on the environmental classification and labelling	18

8	PBT and VPVB assessment	19

8.1	Comparison with criteria from annex XIII	19

8.2	Assessment of substances of an equivalent level of concern	19

8.3	Emission characterisation	19

8.4	Conclusion of PBT and vPvB assessment	19

9	Exposure assessment	20

9.1	General discussion on releases and exposure	20

9.1.1	Summary of the existing legal requirements	20

9.1.2	Summary of the effectiveness of the implemented risk management measures	20

9.2	Manufacturing	20

9.2.1	Occupational exposure	20

9.2.2	Environmental release	20

9.3	“Use 1”	20

9.3.1	Human exposure	20

9.3.1.1	Occupational exposure	20

9.3.1.2	Consumer exposure	20

9.3.2	Environmental release	20

9.4	Other sources (for example natural sources)	20

9.4.1	Human exposure	20

9.4.1.1	Occupational exposure	20

9.4.1.2	Consumer exposure	20

9.4.2	Environmental release	20

9.5	Environmental exposure assessment	20

9.5.1	Summary of emissions	20

9.5.2	Predicted environmental concentrations	20

9.5.2.1	Regional concentrations	21

Atmosphere	21

Aquatic compartment	21

Sediment	21

Soil compartment	21

9.5.2.2	Local concentrations	21

Atmosphere	21

Aquatic compartment	21

Sediment	21

Soil compartment	21

9.5.2.3	Exposure concentrations of man via the environment	21

9.5.3	Measured levels	21

Atmosphere	21

Aquatic compartment	21

Sediment	21

Soil compartment	21

Secondary poisoning	21

9.5.4	Selected environmental concentrations of risk characterisation	21

Atmosphere	21

Aquatic compartment	21

Sediment	21

Soil compartment	21

Secondary poisoning	21

9.6	Combined human exposure assessment	21

10	Risk characterisation	22

10.1	Human health	22

10.1.1	Workers	22

10.1.2	Consumers	22

10.1.3	Indirect exposure of humans via the environment	22

10.1.4	Combined exposures	22

10.2	Environment	22

10.2.1	Aquatic compartment (including sediment and sewage treatment plant and secondary poisoning)	22

10.2.2	Terrestrial compartment (including secondary poisoning)	22

10.2.3	Atmospheric compartment	22

10.2.4	Microbiological activity in sewage treatment systems	22

Information on alternatives	23

11	Information on the risks to human health and the environment related to the manufacture of use of the alternatives	23

12	Availability of alternative, including the time scale	23

13	Technical and economical feasibility	23

Justification for restriction at Community level	24

14	Justification that action is required on the community-wide basis	24

15	Justification for the proposes restriction	24

15.1	Effectiveness	24

15.2	Practicality	24

15.3	Monitorability	24

socio economic assessment	25

other information	26

references	27

TABLES

Table 1: Summary of physico- chemical properties	9

FIGURES

Figure 1: xxxxx	29

EXAMPLES

Example 1 xxxxx	29

Restriction proposal

Substance Name:

EC Number:

CAS number:

Restriction proposal:

Information on hazard and risks

1	identity of the substance and physical and chemical properties

[click here to insert text]

1.1	Name and other identifiers of the substance

| Chemical Name: | Lead Metal |
| --- | --- |
| EC Name: | Lead |
| CAS Number: | 7439-92-1 |
| IUPAC Name: |  |
| Chemical Name: | Lead Oxide |
| EC Name: | Lead Monoxide |
| CAS Number: | 1317-36-8 |
| IUPAC Name: |  |
| Chemical Name: | Lead Tetroxide |
| EC Name: | Orange Lead |
| CAS Number: | 1314-41-6 |
| IUPAC Name: |  |
| Chemical Name: | Dibasic Lead Phthalate |
| EC Name: | Phthalato(2-)]dioxotrilead |
| CAS Number: | 69011-06-9 |
| IUPAC Name: |  |
| Chemical Name: | Basic Lead Sulphate |
| EC Name: | Lead Oxide Sulphate |
| CAS Number: | 12036-76-9 |
| IUPAC Name: |  |
| Chemical Name: | Tribasic Lead Sulphate |
| EC Name: | Tetralead Trioxide Sulphate |
| CAS Number: | 12202-17-4 |
| IUPAC Name: |  |
| Chemical Name: | Tetrabasic Lead Sulphate |
| EC Name: | Pentalead Tetraoxide Sulphate |
| CAS Number: | 12065-90-6 |
| IUPAC Name: |  |
| Chemical Name: | Neutral Lead Stearate |
| EC Name: | Lead Distearate |
| CAS Number: | 1072-35-1 |
| IUPAC Name: |  |
| Chemical Name: | Dibasic Lead Stearate |
| EC Name: | Dioxobis(stearato)trilead |
| CAS Number: | 12578-12-0 |
| IUPAC Name: |  |
| Chemical Name: | Dibasic Lead Phosphite |
| EC Name: | Trilead Dioxide Phosphonate |
| CAS Number: | 12141-20-7 |
| IUPAC Name: |  |
| Chemical Name: | Polybasic Lead Fumarate |
| EC Name: | 2-Butenedioic Acid (E)-, Lead(2+) Salt, Basic |
| CAS Number: | 90268-59-0 |
| IUPAC Name: |  |
| Chemical Name: | Basic Lead Sulphite |
| EC Name: | Sulfurous acid, Lead salt, Dibasic |
| CAS Number: | 62229-08-7 |
| IUPAC Name: |  |
| Chemical Name: | Basic Lead Carbonate |
| EC Name: | Trilead Bis(carbonate) dihydroxide |
| CAS Number: | 1319-46-6 |
| IUPAC Name: |  |

1.2	Composition of the substance

For each constituent/ impurity/ additive, fill in the following table (which should be repeated in case of more than one constituent). The information is particularly important for the main constituent(s) and for the constituents (or impurity) which influence the outcome of the dossier.

| Chemical Name: |  |
| --- | --- |
| EC Number: |  |
| CAS Number: |  |
| IUPAC Name: |  |
| Molecular Formula: |  |
| Structural Formula: |  |
| Molecular Weight: |  |
| Typical concentration (% w/w): |  |
| Concentration range (% w/w): |  |

1.3	Physico-chemical properties

| REACH ref Annex, § | Property | IUCLID section | Value | [enter comment/reference or delete column] |
| --- | --- | --- | --- | --- |
| VII, 7.1 | Physical state at 20°C and 101.3 KPa | 3.1 |  |  |
| VII, 7.2 | Melting/freezing point | 3.2 |  |  |
| VII, 7.3 | Boiling point | 3.3 |  |  |
| VII, 7.4 | Relative density | 3.4 density |  |  |
| VII, 7.5 | Vapour pressure | 3.6 |  |  |
| VII, 7.6 | Surface tension | 3.10 |  |  |
| VII, 7.7 | Water solubility | 3.8 |  |  |
| VII, 7.8 | Partition coefficient n-octanol/water (log value) | 3.7 partition coefficient |  |  |
| VII, 7.9 | Flash point | 3.11 |  |  |
| VII, 7.10 | Flammability | 3.13 |  |  |
| VII, 7.11 | Explosive properties | 3.14 |  |  |
| VII, 7.12 | Self-ignition temperature |  |  |  |
| VII, 7.13 | Oxidising properties | 3.15 |  |  |
| VII, 7.14 | Granulometry | 3.5 |  |  |
| XI, 7.15 | Stability in organic solvents and identity of relevant degradation products | 3.17 |  |  |
| XI, 7.16 | Dissociation constant | 3.21 |  |  |
| XI, 7.17, | Viscosity | 3.22 |  |  |
|  | Auto flammability | 3.12 |  |  |
|  | Reactivity towards container material | 3.18 |  |  |
|  | Thermal stability | 3.19 |  |  |
|  | [enter other property or delete row] |  |  |  |

Table 1: Summary of physico- chemical properties

2	maNufacture and uses

2.1	Manufacture

2.2	Identified uses

2.3	Uses advised against

1

3	classification and labelling

3.1	Classification in Annex I of Directive 67/548/EEC

This should include the classification (including specific concentration limits) listed in Annex I of Directive 67/548/EEC (including the Index Number)

Classification has not been specifically established for the compounds being evaluated in the Risk Assessment. Lead metal, as the powder or in bulk form, is not classified. However, lead compounds not otherwise specified in Annex 1 of Directive 67/548/EEC are classified for the environment as follows:

N; R50-53: Very toxic to aquatic organisms; may cause long-term adverse effects in the aquatic environment.

Repr. Cat. 1; R61 (may cause harm to the unborn child)

Repr. Cat. 3; R62 (possible risk of impaired fertility

Xn; R20/22 (harmful by inhalation and if swallowed)

R33 (danger of cumulative effects)

3.2	Self classification(s)

This should include the classification, the labelling and the specific concentrations limits. The reason and justification for no classification should be reported here.

It should be stated whether the classification is made according to Directive 67/548/EEC criteria or according to GHS criteria.

Environment

At the time of writing [the classification section of the risk assessment report] the OECD Transformation and Dissolution Testing Protocol was undergoing a validation exercise.  Industry had therefore agreed with the Reviewing Country that dissolution testing for lead and lead compounds will be initiated once the results of this validation exercise are available and providing the results are acceptable. Hence no classifications are proposed at this time.

[It should be noted that Transformation and Dissolution testing of lead metal and lead powder is due to commence before the end of 2008].

Health

Physico-chemical properties

Dibasic lead phosphite (CAS 12141-20-7) has recently been experimentally tested acc. to EU method A.10 under GLP, and was characterised as a “highly flammable solid”. Thus, classification with R11 “highly flammable” is proposed.

Health Effects

For reasons specified in detail below, the following health classifications appear as appropriate for inorganic lead compounds.

-	Repr. Cat. 1; R61 (may cause harm to the unborn child)

-	Repr. Cat. 1; R60 (may impair fertility)

-	Cancer Cat. 3; R40 (limited evidence of a carcinogenic effect)

-	Xn; R48/20/22 (danger of serious damage to health by prolonged exposure through inhalation and if swallowed)

The classification for metal powder would be similar to that above, with the exception that no classification would be proposed for carcinogenicity.

Repr. Cat 1; R61 (may cause harm to the unborn child) is supported by the human observational studies detailed in Section 4.1.2.10. This classification is applicable to all inorganic lead compounds. Based upon solubility data, and the probable presence (based upon production process) of lead oxide, extension of this classification to lead metal powder can be considered.

The existing classification of Repr. Cat. 3; R62 (possible risk of impaired fertility) is inadequate in light of human observational studies in Section 4.1.2.10 [of the risk assessment report] which suggest that impacts of inorganic lead compounds upon spermatogenesis occur in human males. Repr. Cat. 1; R60 (may impair fertility) is proposed as the more applicable classification.

Good Laboratory Practice (GLP) and/or guideline compliant data were not found in the published literature for acute oral toxicity. Studies had been conducted in the United States and the EU for seven different stabilizer compounds and reported LD50 values in both male and female rats to be greater than 2000 mg/kg (see Section 4.1.2.3.1 [of the risk assessment report]). The studies were conducted using good laboratory practice and are suitable for the classification of these compounds. The compounds tested include a variety of anions. Literature searches to date have not found information indicating that anions present in compounds not tested will impart properties or toxicity different from those that have been tested. These studies uniformly suggest low potential for acute toxicity via the oral route. Rationale for extension of test data to all compounds covered in this Risk Assessment will be made in a separate derogation document. The recently conducted studies indicate that classification on the basis of acute oral toxicity is not warranted.

A GLP-compliant inhalation toxicity was conducted using lead oxide (see Section 4.1.2.3.1[of the risk assessment report]). Lead oxide was selected for testing based upon dustiness testing (see Section 4.1.1.1.7 [of the risk assessment report]) indicating that it would generate an aerosol with particle size properties intermediate to that expected for other compounds. Pulmonary deposition modelling showed that deposition patterns for all thirteen lead compounds will be rather similar. In detail, deep lung penetration would be minimal and upper respiratory tract deposition would predominate. Upper respiratory tract deposition would in turn be followed by clearance to the gastrointestinal tract. No signs of pulmonary toxicity, irritation or systemic toxicity were evident in the inhalation study. Extension of the lead oxide testing results to the other lead compounds evaluated in this assessment will be addressed in a separate derogation document. However, pulmonary deposition modelling and considerations of chemical properties do not provide a basis for believing that the inhalation toxicity of other compounds will be greater than that of lead oxide.

Based upon the recently conducted oral and inhalation toxicity studies, classification for acute oral and inhalation toxicity (R20/22) is not supported by this Risk Assessment. However, in recognition that chronic and subchronic exposure to inorganic lead compounds has been documented to result in severe health effects in humans, the existing classification of:

-	Xn; R20/22 (harmful by inhalation and if swallowed)

-	R33 (danger of cumulative effects)

Is recommended to be replaced by:

Xn;R48/20/22 (danger of serious damage to health by prolonged exposure through inhalation and if swallowed)

Selected compounds were tested for dermal toxicity (Section 4.1.2.3.1 [of the risk assessment report]), eye irritation and skin irritation (Section 4.1.2.4.1 [of the risk assessment report]) and skin sensitisation (Section 4.1.2.6 [of the risk assessment report]). No evidence for toxicity, irritation or sensitisation was found – classification based upon these acute endpoints is thus not proposed. The derogation strategy for extension of test data from tested to untested substances is outlined in a separate document.

Mutagenicity/Genotoxicity studies (see Section 4.1.2.8 [of the risk assessment report]) with highly soluble lead compounds provide evidence of in vitro mutagenic and genotoxic effects, likely mediated through indirect mechanisms. No consistent indications were found of in vivo effects in experimental animals or exposed humans, especially in studies conducted using physiological routes of compound administration. The concentrations required to produce effects in vitro in most studies exceeds the solubility of the substances of concern to this evaluation. No classification is thus proposed for Mutagenicity for the substances covered in this Risk Assessment.

Carcinogenicity has been demonstrated (see Section 4.1.2.9 [of the risk assessment report]) following the administration of large amounts of highly soluble lead compounds to rodents. Studies, albeit somewhat limited in scope, did not observe carcinogenic effects of lead oxide (inhalation) or lead metal powder (oral and injection). Human epidemiology studies entailing mixed exposures to lead compounds have produced either negative or inconclusive results. Category 3, R40 (limited evidence of a carcinogenic effect) classification for carcinogenicity presently applies to the highly soluble and bioavailable lead acetate and can likely be extended to all lead compounds that will exhibit significant bioavailability after ingestion. Given the large doses of soluble lead compounds required to induce tumours in animals, only compounds with significant bioavailability will likely elicit a carcinogenic response. The bioavailability of most of the lead compounds evaluated in this risk assessment is not known, but the sparingly soluble nature of some of the compounds under consideration does not equate with limited bioavailability under the acidic conditions of the stomach. For example, both lead oxide and lead carbonate exhibit high bioavailability in animal feeding studies and when tested in in vitro gastric simulation systems. While not all of the lead compounds may exhibit high bioavailability, extension of Category 3 R40 classification to all inorganic lead compounds is proposed. This classification would not be extended to lead metal since the bioavailability of lead metal has been demonstrated to be limited and lead metal powder has been tested in an animal carcinogenicity study and did not produce effects.

4	environmental fate properties

4.1	Degradation

4.1.1	Stability

Corresponds to IUCLID 4.1

4.1.2	Biodegradation

4.1.2.1	Biodegradation estimation

4.1.2.2	Screening tests

4.1.2.3	Simulation tests

4.1.3	Summary and discussion of persistence

4.2	Environmental distribution

4.2.1	Adsorption/desorption

Corresponds to IUCLID 4.4.1

4.2.2	Volatilisation

Corresponds to IUCLID 4.4.2

4.2.3	Distribution modelling

4.3	Bioaccumulation

4.3.1	Aquatic bioaccumulation

4.3.1.1	Bioaccumulation estimation

4.3.1.2	Measured bioaccumulation data

4.3.2	Terrestrial bioaccumulation

4.3.3	Summary and discussion of bioaccumulation

4.4	Secondary poisoning

Assessment of the potential for secondary poisoning

5	Human health hazard assessment

5.1	Toxicokinetics (absorption, metabolism, distribution and elimination)

5.2	Acute toxicity

5.2.1	Acute toxicity: oral

5.2.2	Acute toxicity: inhalation

5.2.3	Acute toxicity: dermal

5.2.4	Acute toxicity: other routes

5.2.5	Summary and discussion of acute toxicity

C&L including weight-of-evidence considerations.

5.3	Irritation

5.3.1	Skin

5.3.2	Eye

5.3.3	Respiratory tract

5.3.4	Summary and discussion of irritation

C&L including weight-of-evidence considerations.

5.4	Corrosivity

5.5	Sensitisation

5.5.1	Skin

5.5.2	Respiratory system

5.5.3	Summary and discussion of sensitisation

C&L including weight-of-evidence considerations.

5.6	Repeated dose toxicity

5.6.1	Repeated dose toxicity: oral

5.6.2	Repeated dose toxicity: inhalation

5.6.3	Repeated dose toxicity: dermal

5.6.4	Other relevant information

5.6.5	Summary and discussion of repeated dose toxicity:

C&L, dose-response estimation including weight-of-evidence considerations.

5.7	Mutagenicity

5.7.1	In vitro data

5.7.2	In vivo data

5.7.3	Human data

5.7.4	Other relevant information

5.7.5	Summary and discussion of mutagenicity

C&L, dose-response estimation including weight-of-evidence considerations.

5.8	Carcinogenicity

5.8.1	Carcinogenicity: oral

5.8.2	Carcinogenicity: inhalation

5.8.3	Carcinogenicity: dermal

5.8.4	Carcinogenicity: human data

5.8.5	Other relevant information

5.8.6	Summary and discussion of carcinogenicity

C&L, dose-response estimation including weight-of-evidence considerations.

5.9	Toxicity for reproduction

5.9.1	Effects on fertility

5.9.2	Developmental toxicity

5.9.3	Human data

5.9.4	Other relevant information

5.9.5	Summary and discussion of reproductive toxicity

C&L, dose-response estimation including weight-of-evidence considerations.

5.10	Other effects

5.11	Derivation of DNEL(s) or other quantitative or qualitative measure for dose response

5.11.1	Overview of typical dose descriptors for all endpoints

5.11.2	Correction of dose descriptors if needed (for example route-to-route extrapolation)

5.11.3	Application of assessment factors

5.11.4	Selection/ identification of the critical DNEL(s)/ the leading health effect

6	Human health hazard assessment of physico-chemical properties

6.1	Explosivity

Including C&L

6.2	Flammability

Including C&L

6.3	Oxidising potential

Including C&L

7	Environmental hazard assessment

7.1	Aquatic compartment (including sediment)

7.1.1	Toxicity test results

7.1.1.1	Fish

Short-term toxicity to fish

Long-term toxicity to fish

7.1.1.2	Aquatic invertebrates

Short-term toxicity to aquatic invertebrates

Long-term toxicity to aquatic invertebrates

7.1.1.3	Algae and aquatic plants

7.1.1.4	Sediment organisms

7.1.1.5	Other aquatic organisms

7.1.2	Calculation of Predicted No Effect Concentration (PNEC)

7.1.2.1	PNEC water

7.1.2.2	PNEC sediment

7.2	Terrestrial compartment

7.2.1	Toxicity test results

7.2.1.1	Toxicity to soil macro organisms

7.2.1.2	Toxicity to terrestrial plants

7.2.1.3	Toxicity to soil micro-organisms

7.2.1.4	Toxicity to other terrestrial organisms

Toxicity to birds

Toxicity to other above ground organisms

7.2.2	Calculation of Predicted No Effect Concentration (PNEC_soil)

7.3	Atmospheric compartment

7.4	Microbiological activity in sewage treatment systems

7.4.1	Toxicity to aquatic micro-organisms

7.4.2	PNEC for sewage treatment plant

7.5	Calculation of Predicted No Effect Concentration for secondary poisoning (PNEC_oral)

7.6	Conclusion on the environmental classification and labelling

8	PBT and VPVB assessment

8.1	Comparison with criteria from annex XIII

8.2	Assessment of substances of an equivalent level of concern

8.3	Emission characterisation

8.4	Conclusion of PBT and vPvB assessment

9	Exposure assessment

9.1	General discussion on releases and exposure

9.1.1	Summary of the existing legal requirements

9.1.2	Summary of the effectiveness of the implemented risk management measures

9.2	Manufacturing

9.2.1	Occupational exposure

9.2.2	Environmental release

9.3	“Use 1”

For each use include such a sub-chapter. Subsequently, if there is another “Use 2” this will lead to sub-chapter 9.4 “Use 1” including 9.4.1 Human exposure, 9.4.1.1 Occupational exposure, 7.4.1.2 Consumer exposure and 9.4.2 Environmental release. The other sub-chapters will then be renumbered.

9.3.1	Human exposure

9.3.1.1	Occupational exposure

9.3.1.2	Consumer exposure

9.3.2	Environmental release

9.4	Other sources (for example natural sources)

9.4.1	Human exposure

9.4.1.1	Occupational exposure

9.4.1.2	Consumer exposure

9.4.2	Environmental release

9.5	Environmental exposure assessment

9.5.1	Summary of emissions

9.5.2	Predicted environmental concentrations

9.5.2.1	Regional concentrations

Atmosphere

Aquatic compartment

Sediment

Soil compartment

9.5.2.2	Local concentrations

Atmosphere

Aquatic compartment

Sediment

Soil compartment

9.5.2.3	Exposure concentrations of man via the environment

9.5.3	Measured levels

Atmosphere

Aquatic compartment

Sediment

Soil compartment

Secondary poisoning

9.5.4	Selected environmental concentrations of risk characterisation

Atmosphere

Aquatic compartment

Sediment

Soil compartment

Secondary poisoning

9.6	Combined human exposure assessment

10	Risk characterisation

10.1	Human health

10.1.1	Workers

10.1.2	Consumers

10.1.3	Indirect exposure of humans via the environment

10.1.4	Combined exposures

10.2	Environment

10.2.1	Aquatic compartment (including sediment and sewage treatment plant and secondary poisoning)

10.2.2	Terrestrial compartment (including secondary poisoning)

10.2.3	Atmospheric compartment

10.2.4	Microbiological activity in sewage treatment systems

Information on alternatives

11	Information on the risks to human health and the environment related to the manufacture of use of the alternatives

12	Availability of alternative, including the time scale

13	Technical and economical feasibility

Justification for restriction at Community level

14	Justification that action is required on the community-wide basis

15	Justification for the proposes restriction

15.1	Effectiveness

15.2	Practicality

15.3	Monitorability

socio economic assessment

other information

It is suggested to include here information on any consultation which took place during the development of the dossier. This could indicate who was consulted and by what means, what comments (if any) were received and how these were dealt with. The data sources (e.g registration dossiers, other published sources) used for the dossier could also be indicated here.

The lead industry has, since 2000, been conducting a Voluntary Risk Assessment on Lead and Lead Compounds (VRAL) with the Netherlands government acting in the role of Reviewing Country. The first draft reports were submitted to the European Commission in May 2005 and the dossier was extensively reviewed from March 2006 to April 2008 by the EU Technical Committee for New and Existing Substances. TCNES Opinions on the human health and environment sections are available and SCHER Opinions are pending at the time of writing.

This Annex XV template has been completed and submitted by the Lead Development Association International (co-ordinators of the VRAL) in order to formally hand over to the European Chemicals Agency the VRAL risk assessment reports.  The risk assessment reports themselves are being submitted as the following appendices to this Annex XV handover file:

·	Pb Handover_Annex1_VRAL_Pb_0805_env_sec_poison

·	Pb Handover_Annex2_VRAR_Pb_0804_env_exposure_appendices

·	Pb Handover_Annex3_VRAR_Pb_0804_env_exposure_AppendixC_part2

·	Pb Handover_Annex4_VRAR_Pb_0804_env_exposure_part1

·	Pb Handover_Annex5_VRAR_Pb_0805_env_effects_&_risk_char

·	Pb Handover_Annex6_VRAR_Pb_0805_env_effects_appendices

·	Pb Handover_Annex7_VRAR_Pb_0805_env_exposure_part2

·	Pb Handover_Annex8_VRAR_Pb_0803_hh

The attached versions of the risk assessment reports are the final versions and have previously been circulated to TCNES and sent to SCHER for review.

references

[click to insert references classed alphabetically by author. For details on referencing, see explanatory note]

Annex

[click here to insert text, or delete heading as appropriate]

Figure 1: xxxxx

Example 1 xxxxx

Frghfhgfdhdf